## Slide 1
Multi Agentic Energy Trading
Team: Abhiraj · Chethana SB · Ashna Satrasala.

## Slide 2
Problem Statement — Why this matters
By end-2025 India reached ~20.8 GW rooftop solar, yet grid operators discarded an estimated 2.3 TWh of solar while paying ~₹6,000 crore in must‑run compensation. The issue is not lack of demand but the absence of a direct, low‑latency mechanism for neighbours to trade surplus energy. Traditional cloud auctions and public blockchains fail to meet residential latency, privacy and scalability requirements.

## Slide 3
Solution Overview
We propose a complete local-edge energy trading platform where autonomous agents negotiate real‑time prices, satellite‑informed forecasts run via federated learning to preserve privacy, grid feasibility is validated locally, and settlements are recorded on a dual‑tier local blockchain. Key results: 20% reduction in wasted solar, 22.5% cluster efficiency improvement, low‑latency trading, privacy‑preserving forecasts, and secure local settlements.
Low Latency
Local negotiation and communication minimize delays for 15‑minute interval trading.
Privacy
Federated Learning trains models without sending raw household data offsite.
Secure Settlements
Local Ethereum (Hardhat) nodes provide immutable transaction records for trust.

## Slide 4
Technology Stack
The system integrates: Edge Computing, Multi‑Agent AI, Federated Learning, Blockchain, IoT energy monitoring, Power‑system optimization, Satellite data analytics (Sentinel‑2), and Real‑time communication. These layers work together to forecast, negotiate, validate and settle trades within a local cluster.

## Slide 5
Hardware & System Architecture — Components
Architecture consists of: (1) Cluster Server (shared edge), (2) Household Nodes, (3) Local Communication Network, (4) Satellite Data Integration Layer, (5) Blockchain Settlement Layer. The Cluster Server hosts forecasting, negotiation, validation and blockchain services while household nodes provide sensing, control and local actuation.
Cluster Server
Shared edge system hosting multi‑agent engine, FL server, OPF engine, blockchain node and real‑time comms.
Household Node
ESP32 microcontroller coordinates local sensors, relays and communicates with the cluster server.
Local Network
TP‑Link EAP225 forms the LAN for low‑latency, internet‑independent communication across the cluster.

## Slide 6
Cluster Server — Internal Modules
Multi‑Agent AI Engine
Creates an autonomous agent per household to negotiate trades, set prices and optimise allocations across the cluster in real time.
Language Model Module
Supports agent reasoning, improves coordination, enables contextual and adaptive negotiation strategies.
Federated Learning Server
Trains distributed forecasting models on local data, preserving privacy and improving prediction accuracy without sharing raw data.
Power System Analysis Engine
Runs Optimal Power Flow (OPF) to validate physical grid feasibility and prevent overloads before trades are approved.
Blockchain Node
Private Ethereum (Hardhat) node records validated transactions for transparency and immutable settlement records.
Real‑Time Communication Server
Provides low‑latency messaging, dashboard updates and synchronisation across household nodes.

## Slide 7
Household Node — Devices & Functions
PZEM‑004T Sensor
Measures voltage, current and calculates instantaneous power for generation and consumption monitoring.
4‑Channel Relay
Controls household loads for demand response and executes switching based on trading outcomes.
ESP32 Controller
Acts as the household controller: collects sensor data, executes control commands, and communicates with the cluster server.

## Slide 8
Energy Trading Workflow (15‑minute rounds)
Validate
Negotiate
Forecast
Transmit
Measure
Process summary: (1) PZEM sensors measure; (2) ESP32 sends data to Cluster; (3) forecasting estimates demand & generation; (4) agents negotiate trades; (5) OPF validates grid constraints; (6) approved trades finalised; (7) transactions written to local Ethereum; (8) dashboards update in real time.

## Slide 9
Cost Analysis — Per Household & Shared Infrastructure
Per Household Component
Cost (INR)
PZEM‑004T Energy Sensor
₹534
ESP32 Microcontroller
₹249
4‑Channel Relay Module
₹249
Share of Mini‑PC Cost
₹2,800
Share of Wi‑Fi Access Point
₹506
Total per Household
₹4,338
Shared Infrastructure
Cost (INR)
Beelink SER5 Mini‑PC
₹28,000
TP‑Link EAP225 Access Point
₹5,059

## Slide 10
Proof of Concept, Social Impact & Conclusion
Proof of Concept
Web demo: https://p2p-trading-nrj4iz7e0-abhirajs-projects-1d7aabae.vercel.app/ · Video demo: https://drive.google.com/file/d/17HzW5DpCWRaoFsLILpnOXY-AOs39rTaz/view
Social Impact
Reduces renewable energy wastage, lowers household electricity costs, promotes community energy independence, preserves privacy via federated learning and builds trust through transparent blockchain settlements — supporting India’s clean energy goals.
Conclusion
By combining Edge Computing, Multi‑Agent AI, Federated Learning, IoT sensing, Satellite Analytics, Power‑system Optimization and Blockchain, the platform enables real‑time local energy exchange, reduces waste, improves efficiency and accelerates residential adoption of sustainable energy.